IOMMU Driver Consolidation
Joerg Roedel <jroedel@suse.de>

---
Make Drivers Behave Consistently
- Semantics for assigning and de-assigning devices
- Differences in how many devices can be in a domain
- Visible through the IOMMU-API

---
Introducing a Default Domain
- Allocate a default domain for each group of devices
- Put every device into its default domain initially
- When device is de-assigned from an arbitrary domain it is put back into the default domain
- Default domain will be used for common DMA-API implementation

---
Common DMA-API Implementation
- Currently x86 drivers have their own implementation
- There is a common DMA-API implementation for ARM
  - Uses the IOMMU-API already
  - Not suitable as-is for x86 IOMMUs
- We want to have a single one for all IOMMU drivers
  - Requires extension to the IOMMU-API (iommu_commit)
  - Should suit ARM as well as x86 and all other platforms
  - Requires consistent behavior of IOMMU drivers

---
Factor out Common Code
- Candidates:
  - Factor out handling of indidividual IOMMU hardware devices to the IOMMU core
  - Manage the device->IOMMU relationship
  - Keep track of IOTLB flushing in the IOMMU core

---
Doing it Step by Step
- Idea is to handle the transition of drivers to new IOMMU core features incrementally
- Add feature reporting to IOMMU drivers
- By reporting features (or the lack of) IOMMU drivers can delegate functionality to the IOMMU core
- Allows to introduce the core changes and then adapt drivers step by step